## Slide 1: Application of Transformers for Oil Well Production Forecasting
Pedro Henrique Cardoso Paulo
Felipe da Costa Pereira
Helon Vicente Hultmann Ayala

## Slide 2: agenda
- Problem description
- Literature review
- Dataset
- Methods
- Results
- Concluding Remarks
- Future work

## Slide 3: Problem description
Flow rates estimation: Characteristics and Limitations
  On a oil and gas production system, the production from each well is uncertain
  Well rate is an apportionment of the total production
  Measures need to be made after phase separation, one well at a time: test separator
  Alternative: multiphase flowmeters
    Associated error, calibration is a challenge;
    Pressure drop, production loss;
    Not accepted by ANP;
    One per well, expensive
Impacts
  Unreliable production history (3-D simulator input)
  Poor capacity to take reservoir management decisions
[Tracerco.com - Johan Castberg Field, offshore Norway]
Offshore Production system
3-Phase separator vessel (oil/water/gas)
[arab-oil-naturalgas.com]
Multiphase Flowmeter [krohne.com]

## Slide 4: Literature review RATE PREDICTIONS
Paper | Input | Output | Method | Simulation | Data
Alakeely, Horne [2021] | Surface measures Choke, GOR, WHP | Liquid/Oil rate Water cut | Neural Network, Autoencoders | Free response | Well 15/9-F-14 (Volve)
Jouradanou et al. [2019] | Valves position | Pressures (riser inlet and bottom-hole) | Echo State Network | Free response | OLGA(*)
Aguirre et al. [2017] | Various Process variables | BHP | MLP, NARMAX, NFIR, Kalman filters | Free response | Real wells (Petrobras)
Freitas et al. [2021] | Gas lift Flow Rate | BHP | MLP Steady State response | Free response | 2 simulated systems, 1 Deep water oil well
Apio et al. [2019] | Tubing Pressure Riser Pressure | BHP | Kalman Filters | Free response | 2 OLGA(*) cases 1 real well (Petrobras)
Liu et al. [2022] | No input (auto-regressive) | Oil Rate | ESN + GA | Short term forecast (15%) | 2 China + 1 US oil Fields
(*) OiL and GAs dynamic multiphase flow simulator

## Slide 5: Literature review TRANSFORMERS FOR Time series
(*) OiL and GAs dynamic multiphase flow simulator
Pazouki and Farsani (2020) used an adapted version of the architecture in multiple benckmark datasets and obtained better or equivalent results when compared to other methods
Zerveas et al. (2021) proposed a generalistic framework for working with multivariate time series using the architecture
  Use unsupervised pre-training of the network in autoregression tasks
  Applied the proposed architecture to various time series problems, obtaining better or close results when compared to other methodologies

## Slide 6: dataset
Dataset Volve Field Data
www.equinor.com
Volve Field Dataset
Production history, geological data and reservoir model provided by Equinor
Disclosed in 2018 by Equinor
6 production wells + 1 water injector well
Available well data:
  Temperature and Pressures
    Well head, X-mas Tree and bottomhole
  Choke openings and pressure drop
  Oil, water and gas rates

## Slide 7: Methods: Transformer architecture
Data input (6 x memory)
Transformer Encoder Layer
Linear Layer (6 x 1)
Predicted value (1x memory)
Fully-Connected Layers with ReLU Activation (6 x 6)
Nenc layers
Nfc layers
Input masking (train only)
DL Framework: PyTorch
Input comprised of input variables and output variable, all delayed one timestep from prediction
Both Nenc and Nfc can be varied (base case is 1 and 0)
Memory comprises the number of vectors provided to the attention mechanism (base case is 16)
Statistical analisys performed
  Nenc from 1 to 4
  Nfc from 0 to 2
  Memory from 4 to 32
  10 runs for each model
Some hyperparameters were kept constant in all performed tests
  Dropout kept in 10%
  Transformer feedforward dimension kept in 12

## Slide 8: Methods: NUMERICAL EXPERIMENT PIPELINE (SYSID)

## Slide 9: Methods: NUMERICAL EXPERIMENT PIPELINE (TRANSFORMER)
Read data
Select input variables
Select output
Normalize data
Divide by q95
Create data windows
Input containing input and output variables of the previous timestep
Consider only train data
Split the data
60% train
10% validation
20% test
Create batches
4 Windows in each batch
Train the network
Optimizer: AdamW
LR: 5 x 10-4
Patience: 20 epochs
Evaluate model
RMSE
R2
Loss: MSE (considering full window)

## Slide 10: Results Overall results

## Slide 11: Results statistical analisys

## Slide 12: Results TRANSFER LEARNING
No data form the benchmark well seen during training
More encoder layers added due to more data available (4 layers)
Good agreement in OSA prediction, but poor performance in FS
More tests needed

## Slide 13: Concluding remarks
Transformer model outperforms the other models considered
  Demand less parameters than the FC NN
  Valid for the base case model
Statistical analysis showed low impact of the memory window
  More encoder layers caused more outliers (maybe we do not have enough data)
  Average base model is better than the average tested model
  FS standard deviation is very similar in all models and base model
Transfer learning showed promising results in OSA prediction
  Poor results in FS
  More studies are needed

## Slide 14: Future work
Improve the variance of the model, reducing the dispersion
Improve architecture in order to viabilize the transfer learning strategy for Free-run simulations
Work with dimensional data, eliminating the normalization timestep
Include other similar benchmark datasets in the pipeline, such as the SPE Dataset